## Slide 1: Build an Autonomous Robot with bcr_bot + Nav2
Use ready-made ROS 2 packages, understand the algorithms inside them, and adapt them to a real robot that drives itself to “Table 1”
ROS 2 · Gazebo · SLAM Toolbox · Nav2 · ESP32 · RPLidar
Notes: Welcome. In this course students do NOT design a robot from scratch. They take a ready-made ROS 2 robot package (bcr_bot, from Black Coffee Robotics), open-source navigation (Nav2) and mapping (SLAM Toolbox), and learn (1) how those packages are built, (2) which algorithms run inside them, and (3) exactly what must change to run them on our physical robot: an ESP32 with two DC gear motors and encoders plus an RPLidar A1. The final goal of the lab: open a web page on a phone, tap “table1”, and the robot drives there by itself.

## Slide 2: Course map: five modules
01
The big picture
What autonomy means, the software stack we reuse, and ROS 2 basics
02
Inside bcr_bot
Folders, build system, URDF / Xacro, Gazebo plugins, launch files and TF
03
The algorithms
Kinematics, odometry, SLAM, AMCL, costmaps, planning, control, behavior trees
04
Simulation → real robot
What changes when Gazebo is replaced by an ESP32, motors and an RPLidar
05
Hands-on lab
Bring-up, calibration, mapping, navigation and the “go to Table 1” web app
Final result: a student taps “table1” on a phone, and the real robot plans a path and drives to Table 1 by itself.
Notes: The course is split into five modules. Modules 1–3 are theory with live demos (simulation or RViz). Module 4 explains the gap between simulation and the real robot, using the real mistakes we found in our own code. Module 5 is the hands-on lab, done in six checked steps. Suggested timing: 1 session each for modules 1–2, 2 sessions for module 3, 1 for module 4 and 2–3 lab sessions.

## Slide 3: The big picture
01
What makes a robot autonomous, and which ready-made packages do the work
Notes: Module 1 sets the vocabulary. Students should leave knowing the sense–localize–plan–act loop, which package does which job, and the eight ROS 2 concepts used everywhere later.

## Slide 4: An autonomous robot repeats one loop: sense, localize, plan, act
Sense
What is around me?
RPLidar distances on /scan and wheel encoder ticks
Localize
Where am I on the map?
slam_toolbox while mapping, AMCL while navigating
Plan
Which way to the goal?
Nav2 planner searches the global costmap
Act
How do the wheels move?
Controller → /cmd_vel → ESP32 → motors
Repeats about 20 times per second (controller_frequency: 20 Hz)
Notes: Every autonomous mobile robot runs this loop many times per second. Sense: read the sensors (LiDAR distances and wheel encoder ticks). Localize: work out where the robot is on the map (SLAM Toolbox while mapping, AMCL during navigation). Plan: find a collision-free path to the goal on a costmap. Act: turn the path into wheel speeds (Nav2 controller → /cmd_vel → ESP32). Ask students which step fails if the LiDAR is unplugged (all of them!), and which step is responsible if the robot knows where it is but hits a chair (plan/act with the costmap).

## Slide 5: We reuse a stack of open-source packages and write only the glue
Application
table_nav_web — phone web page: “go to table1”
WE WROTE
Navigation
Nav2 — planner, controller, costmaps, behavior tree, AMCL
REUSED
Mapping
slam_toolbox — builds the map from LiDAR scans
REUSED
Robot package
bcr_bot — URDF, worlds, launch files, nav2_params.yaml
MODIFIED
Drivers & odometry
sllidar_ros2 (LiDAR) · esp32_driver (motors + encoders) · rf2o
REUSED + OURS
Hardware
ESP32 · MDD10A motor driver · 2 DC gear motors + encoders · RPLidar A1
BUILT
Notes: Read the stack from the bottom up. Hardware: ESP32 microcontroller, MDD10A motor driver, two DC gear motors with encoders, RPLidar A1. Drivers: sllidar_ros2 publishes /scan; our esp32_driver node (my_python_pkg) converts /cmd_vel to wheel speeds and encoder ticks to /odom; rf2o can estimate odometry from laser scans. bcr_bot provides the robot model, simulation worlds, launch files and Nav2 parameters. SLAM Toolbox makes maps, Nav2 navigates. On top, table_nav_web is a small web app we wrote. Key message: professionals rarely write SLAM or path planners from scratch; the engineering work is configuration, calibration, integration and testing.

## Slide 6: Eight ROS 2 ideas you need before touching Nav2
Node
A running program with one job
esp32_driver
sllidar_node
Topic
Stream of messages: publish / subscribe
/scan /odom /cmd_vel
Service
Request → one reply
/map_server/load_map
Action
Long task with feedback and cancel
navigate_to_pose
Parameter
A setting of a node, loaded from YAML
desired_linear_vel: 0.18
Launch file
Python script that starts many nodes
nav2.launch.py
TF
Where each frame is relative to another
map → odom → base_link
Package + colcon
Folder of code and config; colcon builds it
colcon build
Notes: Spend time here: everything later is described with these words. Node = one running program (e.g. esp32_driver). Topic = a named stream of messages; many publishers/subscribers; e.g. /scan, /odom, /cmd_vel. Service = request and one reply. Action = long-running goal with feedback and the possibility to cancel — Nav2 navigation is an action (navigate_to_pose). Parameter = a setting of a node, usually loaded from a YAML file such as nav2_params.yaml. Launch file = Python script that starts many nodes with their parameters. TF = the tree of coordinate frames (map, odom, base_link, laser). Package + colcon = how code and config are organised and built. Quick demo: ros2 node list, ros2 topic list, ros2 topic echo /odom.

## Slide 7: Inside the bcr_bot package
02
How a ready-made ROS 2 robot package is organised, built and launched
Notes: bcr_bot (github.com/blackcoffeerobotics/bcr_bot) is a simulation package for a warehouse differential-drive robot. It supports Gazebo Classic, Gazebo Fortress/Harmonic and Isaac Sim. We use it as a template: its structure, launch files and Nav2 configuration are reused and adapted for our real robot.

## Slide 8: bcr_bot is a normal ROS 2 package: every folder has one job
bcr_bot/
├── package.xml # name, version, dependencies
├── CMakeLists.txt # what gets installed
├── urdf/ # robot model (xacro)
├── meshes/ # 3D shapes for visuals
├── worlds/ # Gazebo worlds (.sdf)
├── models/ # warehouse objects
├── launch/ # start-up scripts (.py)
├── config/ # nav2 + slam params, map
├── rviz/ # saved RViz views
└── scripts/ # remapper.py (sim only)
Describe the robot
urdf/ meshes/
Links, joints, sensors and where they are mounted
Simulate the world
worlds/ models/ urdf/gazebo.xacro
Warehouse world and the Gazebo plugins
Run & configure
launch/ config/ rviz/
What starts, and with which parameters
Notes: Open the folder in VS Code while explaining. package.xml and CMakeLists.txt make it a ROS 2 package. urdf/ describes the robot, meshes/ gives it a 3D look, worlds/ and models/ build the Gazebo warehouse, launch/ starts everything, config/ holds the parameters (nav2_params.yaml, mapper_params_online_async.yaml) and the map, rviz/ stores RViz views, scripts/ holds remapper.py which is only needed in simulation. Ask students: which folders matter on the real robot? (launch, config, and the TF information from urdf.)

## Slide 9: From source folder to ros2 launch: how the package is built
package.xml
declares the dependencies
CMakeLists.txt
install(DIRECTORY …) lists folders to copy
colcon build
copies files into install/
install/share/
bcr_bot
what ROS actually reads
ros2 launch
reads files from the install folder
# build the workspace
mkdir -p ~/ros2_ws/src && cd ~/ros2_ws/src
git clone -b real-robot-nav-web-app \
https://github.com/febintjames/autonomousrobot.git
cd ~/ros2_ws
rosdep install --from-paths src --ignore-src -r -y
colcon build --symlink-install
source install/setup.bash
# CMakeLists.txt (bcr_bot)
install(DIRECTORY launch meshes models
urdf worlds rviz
DESTINATION share/${PROJECT_NAME}/)
install(DIRECTORY config/ DESTINATION
share/${PROJECT_NAME}/config)
install(PROGRAMS scripts/remapper.py
DESTINATION lib/${PROJECT_NAME})
Tip: with --symlink-install, edits to existing launch and config files work without rebuilding; new files still need colcon build.
Notes: Explain the build pipeline. package.xml lists dependencies so rosdep can install them. CMakeLists.txt says which folders to copy (install). colcon build copies them into install/share/bcr_bot. Launch files never read your src folder: they call get_package_share_directory("bcr_bot"), which points into install/. That is why students who edit nav2_params.yaml and do not rebuild see no change — unless they built with --symlink-install, which links installed files back to src (new files still need a rebuild). Live demo: run colcon build, then ls install/bcr_bot/share/bcr_bot.

## Slide 10: The robot model: links connected by joints, written in Xacro
base_footprint
base_link
chassis_link fixed
middle_left_wheel continuous
middle_right_wheel continuous
front/back wheels ×4 fixed
two_d_lidar fixed
imu_frame fixed
kinect_camera fixed
<xacro:property
name="traction_wheel_radius" value="0.1"/>
<xacro:property
name="traction_track_width" value="0.6"/>
<xacro:arg name="two_d_lidar_enabled"
default="false"/>
<xacro:traction_wheel dexterity="left"
origin_y="${traction_track_width/2}"/>
Link = rigid part with visual, collision and inertia
Joint = how two links connect: fixed, continuous (wheels), revolute
Xacro = URDF + variables, macros and if-switches: one file, many robot variants
Notes: URDF describes the robot as a tree of links (rigid bodies with visual, collision and inertial parts) connected by joints. bcr_bot.xacro uses Xacro, which adds variables (xacro:property), arguments (xacro:arg, e.g. two_d_lidar_enabled), if-switches and macros (traction_wheel, trolley_wheel) so one file can describe many variants. Wheels that turn are continuous joints; sensors are fixed joints. robot_state_publisher reads this model and publishes the fixed transforms, e.g. base_link → two_d_lidar. Our physical robot is smaller (≈0.38 m wide, wheel radius 0.0425 m), so on the real robot we publish base_link → laser with a static transform instead of using this 0.9 m warehouse model.

## Slide 11: Gazebo plugins turn the model into a virtual robot
Plugin (urdf/gazebo.xacro) | What it simulates | ROS 2 interface
libgazebo_ros_diff_drive | Two driven wheels: turns cmd_vel into motion and reports odometry | sub cmd_vel · pub odom + TF
libgazebo_ros_ray_sensor | 2D LiDAR: 361 rays, 30 Hz, 0.55–16 m | pub scan
libgazebo_ros_imu_sensor | IMU (gyro + accelerometer), 5 Hz | pub imu
libgazebo_ros_camera | Kinect depth camera and stereo camera | pub image + depth topics
libgazebo_ros_p3d | Exact ground-truth pose for debugging | pub p3d_ground_truth
odometry_source:=world makes Gazebo report PERFECT odometry. Real wheels slip and encoders miscount, so a robot that drives perfectly in simulation can wander on a real floor. On the real robot every plugin above is replaced by a real driver (Module 4).
Notes: urdf/gazebo.xacro attaches plugins to the model. The diff_drive plugin subscribes to cmd_vel, moves the two traction wheels and publishes odometry plus the odom → base_footprint transform. The ray sensor plugin simulates the 2D LiDAR (361 rays, 30 Hz, 0.55–16 m). IMU and camera plugins publish sensor data. p3d publishes the exact ground-truth pose (topic p3d_ground_truth). In simulation all topics are under the /bcr_bot namespace (e.g. /bcr_bot/scan). The big lesson is the callout: odometry_source:=world gives perfect odometry, so things that work in simulation can fail on the real floor.

## Slide 12: Five launch commands run the whole system
Command | What it starts | Use it for
ros2 launch bcr_bot gazebo.launch.py | Gazebo, warehouse world, robot_state_publisher, spawn_entity | Simulation only
ros2 launch bcr_bot robot_bringup.launch.py | RPLidar driver, base_link → laser TF, ESP32 motor + odometry driver | Real robot (new)
ros2 launch bcr_bot mapping.launch.py | slam_toolbox (online async) + RViz | Making a map
ros2 launch bcr_bot nav2.launch.py map:=… | map_server, AMCL, planner, controller, BT navigator, RViz | Navigating
ros2 launch table_nav_web table_nav_web.launch.py | Web server on port 8080 | Going to tables
Launch arguments (no file editing): two_d_lidar_enabled:=True map:=$HOME/maps/my_map.yaml use_rviz:=False
Notes: Launch files are Python scripts that start nodes with parameters. gazebo.launch.py starts Gazebo, loads small_warehouse.sdf and spawns the robot (robot_state_publisher + spawn_entity). robot_bringup.launch.py is new: it is the real-robot replacement for Gazebo. mapping.launch.py includes slam_toolbox online_async_launch.py with our mapper_params_online_async.yaml. nav2.launch.py includes nav2_bringup bringup_launch.py with our map and nav2_params.yaml. Arguments after := change behaviour without editing files, for example: ros2 launch bcr_bot gazebo.launch.py two_d_lidar_enabled:=True camera_enabled:=False.

## Slide 13: TF: every frame has one parent and exactly one publisher
map
odom
base_link
laser
AMCL (navigation) or slam_toolbox (mapping)
corrects drift — may jump
esp32_driver (encoders) OR rf2o (laser)
smooth — drifts slowly — exactly ONE
static transform (robot_bringup / URDF)
where the LiDAR is mounted
Rules students forget
Only ONE node may publish each transform. Two odometry publishers make the pose flicker.
map → odom appears only after AMCL gets an initial pose.
A wrong laser yaw puts obstacles behind the robot.
Check: ros2 run tf2_tools view_frames
Notes: TF is the most common source of real-robot bugs. map is the fixed world frame; map → odom is published by AMCL (navigation) or slam_toolbox (mapping) and corrects odometry drift, so it can jump. odom → base_link is published by the odometry node (our esp32_driver from encoders, or rf2o from laser) — smooth but slowly drifting. base_link → laser is a fixed transform describing where the LiDAR is mounted. Show students ros2 run tf2_tools view_frames and ros2 run tf2_ros tf2_echo map base_link. Ask: what happens if both esp32_driver and rf2o publish odom → base_link? (The pose flickers between two estimates and the robot jerks — we had exactly this bug.)

## Slide 14: The algorithms
03
What each package computes — with the formulas and the parameter values we use
Notes: Module 3 opens the black boxes. For each algorithm: the idea in one sentence, the formula or picture, and the parameter in our configuration that controls it. Students do not need to implement these, but they must understand them to tune and debug the robot.

## Slide 15: Differential drive: two wheel speeds give any forward and turning speed
v_l
v_r
v, ω
W = wheel separation = 0.34 m
forward
Robot → wheels (esp32_driver)
v_l = v − ω·W/2
v_r = v + ω·W/2
Wheels → robot (odometry)
v = (v_r + v_l)/2 ω = (v_r − v_l)/W
Example: v = 0.18 m/s, ω = 0.5 rad/s → v_l = 0.095 m/s, v_r = 0.265 m/s, turn radius R = v/ω = 0.36 m
Speed limit? Scale v and ω together — clamping one changes R and the curve.
Notes: Our robot has two driven wheels and a caster. Nav2 sends v (m/s forward) and ω (rad/s turning) on /cmd_vel. The driver converts them: v_l = v − ω·W/2 and v_r = v + ω·W/2, where W is the wheel separation. Odometry does the reverse. Worked example on the slide: v = 0.18, ω = 0.5, W = 0.34 → left wheel 0.095 m/s, right wheel 0.265 m/s, turning radius v/ω = 0.36 m. Important lesson from our robot: if you must limit speed, scale v and ω by the same factor; clamping them separately changes v/ω, the turning radius, so the robot drives a different curve than Nav2 planned. This code is in esp32_teleop_odometry_node.py, cmd_vel_cb.

## Slide 16: Wheel odometry: count encoder ticks and add up the motion
1
Ticks per wheel turn
7 PPR × 19.2 gearbox × 4 (quadrature) = 537.6
2
Metres per tick
2π × 0.0425 m ÷ 537.6 ≈ 0.50 mm
3
Wheel distances
d_L, d_R = Δticks × metres per tick
4
Robot motion
d = (d_R + d_L)/2 Δθ = (d_R − d_L)/W
5
New pose
x += d·cos(θ + Δθ/2) y += d·sin(θ + Δθ/2) θ += Δθ
Why odometry drifts
2 % wheel-size error → 2 cm wrong every metre
3 % track-width error → ≈11° heading error per full turn
Wheel slip, soft tyres and gearbox backlash
Errors never reset — AMCL corrects them using the map
Publishes /odom and TF odom → base_link
Notes: Odometry integrates small motions. Ticks per wheel revolution: 7 pulses × 19.2 gearbox × 4 (quadrature, counting both edges of both channels) = 537.6. One tick is 2π·0.0425/537.6 ≈ 0.50 mm of travel. Every encoder message (~30 Hz) the driver computes left and right distances, the robot’s forward motion d and rotation Δθ, and adds them to the pose using the mid-point heading. Errors accumulate forever: a 2 % wheel-size error is 2 cm per metre; a 3 % track-width error is about 11° per full turn. That is why we calibrate (lab step 3) and why AMCL uses the map to correct drift.

## Slide 17: LiDAR measures distances all around; rf2o turns scan changes into motion
table
shadow behind the table
# sensor_msgs/LaserScan on /scan
header.frame_id: laser
angle_min: -3.14 angle_max: 3.14
angle_increment: 0.0175 # 1 degree
range_min: 0.15 range_max: 12.0
ranges: [2.31, 2.29, 2.30, inf, ...]
rf2o laser odometry
Compares consecutive scans to estimate dx, dy, dθ
No wheels needed, not fooled by wheel slip
Weak in long empty corridors; needs fast scans
Choose ONE: odom_source:=wheel | laser
Notes: The RPLidar spins a laser and reports one distance per angle — a sensor_msgs/LaserScan message on /scan. With angle_compensate on we get roughly 360 rays, one per degree, range 0.15–12 m, several scans per second (check with ros2 topic hz /scan). The picture shows a scan in a room: rays stop at walls, and the table casts a shadow where the LiDAR cannot see. rf2o (range-flow odometry) compares two consecutive scans and estimates how the robot moved — useful when wheels slip, but weak in long featureless corridors. Use only one odometry source: robot_bringup.launch.py has odom_source:=wheel (default) or odom_source:=laser.

## Slide 18: SLAM Toolbox builds the map and localizes at the same time
loop closure
● pose node — odometry / scan-match edge - - loop closure
1
Scan matching
Align each new scan with recent ones → a better pose than odometry
2
Add a node
Every 0.15 m or 0.15 rad of travel (minimum_travel_distance / heading)
3
Loop closure
Recognise a place seen before (do_loop_closing: true)
4
Optimize the graph
Ceres solver spreads the accumulated error over all nodes
5
Publish
/map (5 cm occupancy grid) and the map → odom transform
Notes: SLAM = Simultaneous Localization And Mapping. SLAM Toolbox is graph-based: every time the robot moves 0.15 m or turns 0.15 rad it stores a node (pose + scan). Scan matching aligns each new scan with recent scans, which gives a better pose than odometry alone. When the robot returns to a place it has seen, loop closure adds an extra constraint (orange dashed edge) and the Ceres optimizer moves all nodes so the constraints agree — this removes accumulated drift. Finally the scans are rendered into an occupancy grid (/map, 5 cm cells) and the map → odom transform is published. Our parameters are in bcr_bot/config/mapper_params_online_async.yaml.

## Slide 19: A map is an occupancy grid: free, occupied or unknown cells
occupied (0)
free (254)
unknown (205)
1 cell = 5 cm × 5 cm
image: my_map.pgm # the picture
mode: trinary
resolution: 0.05 # metres per pixel
origin: [-2.1, -3.4, 0] # bottom-left pixel
occupied_thresh: 0.65 # darker → occupied
free_thresh: 0.25 # lighter → free
bcr_map.yaml is the Gazebo warehouse (29 × 31 m). On the real robot AMCL then matches your room against shelves that do not exist. Always make and load a map of YOUR room.
Notes: map_saver_cli writes two files: a .pgm picture and a .yaml description. Each pixel is one cell (resolution 0.05 m = 5 cm). Dark pixels are occupied, light pixels free, mid-grey unknown (never seen). origin is the world position of the bottom-left pixel, which is how a pixel becomes x, y in metres. Show students both files in a text editor and an image viewer. Then the warning: bcr_bot ships bcr_map.yaml, which is the Gazebo warehouse (29 × 31 m). Our nav2.launch.py used it by default, so AMCL compared our classroom to warehouse shelves — the main reason the real robot moved badly.

## Slide 20: AMCL: a particle filter finds where the robot is on the map
1 · Predict
The robot moved 0.25 m: move every particle the same way, plus random noise.
2 · Weight
Compare the real scan with what each particle would see. Good match → heavy particle.
3 · Resample
Keep heavy particles, drop light ones. The cluster is the pose → map → odom.
Notes: AMCL (Adaptive Monte Carlo Localization) keeps hundreds of guesses (particles) of the robot pose. Predict: when odometry says the robot moved, every particle moves the same way plus random noise (alpha1–alpha5). Weight: for each particle, AMCL checks how well the real LiDAR scan fits the map if the robot were there (likelihood field model) — good fit, high weight. Resample: draw a new particle set favouring heavy particles; the cluster is the pose estimate and AMCL publishes map → odom. Our values: 500–2000 particles, update after 0.25 m or 0.2 rad, laser range 0.2–12 m. Students must give AMCL an initial pose (RViz 2D Pose Estimate or the web app “Robot is here”), otherwise particles start in the wrong place.

## Slide 21: Costmaps: the map, live obstacles and a safety margin in one grid
Static layer
walls from /map
+
Obstacle / voxel layer
what the LiDAR sees now
+
Inflation layer
safety margin around obstacles
=
Costmap
what the planner and controller use
Global costmap
frame: map — the whole map
layers: static + obstacle + inflation
used by the planner · updates 1 Hz
Local costmap
frame: odom — 3 × 3 m around the robot
layers: voxel + inflation
used by the controller · updates 5 Hz
Cost value of a cell
0
free
1–252
inflated
253
inscribed
254
lethal
255
unknown
Notes: Nav2 never plans on the raw map. It builds costmaps by stacking layers: the static layer copies walls from /map; the obstacle (or voxel) layer marks what the LiDAR sees now — people, chairs, bags — and clears cells when the laser passes through them; the inflation layer adds a cost that falls off with distance from every obstacle, so paths keep a safety margin. There are two costmaps: global (whole map, for the planner) and local (a 3 × 3 m window that moves with the robot, for the controller). Cost values: 0 free, 1–252 inflated, 253 inscribed (the robot would touch), 254 lethal (an obstacle), 255 unknown. robot_radius must be the real robot size and identical in both costmaps — ours was wrong (0.12 m local vs 0.22 m global).

## Slide 22: Inflation: cost falls with distance from an obstacle
Chart: Cell cost vs distance from obstacle
| 0.00 | 0.05 | 0.10 | 0.15 | 0.20 | 0.25 | 0.30 | 0.35 | 0.40 | 0.45 | 0.50 | 0.55 | 0.60
cost_scaling_factor 3 (ours) | 254 | 253 | 253 | 253 | 253 | 230 | 198 | 171 | 147 | 126 | 109 | 94 | 0
cost_scaling_factor 10 | 254 | 253 | 253 | 253 | 253 | 187 | 113 | 69 | 42 | 25 | 15 | 9 | 0
cost = 252 · e^(−k·(d − r))
r = robot_radius 0.22 m, k = cost_scaling_factor
d ≤ 0.22 m → 253: robot would touch, never planned
d > 0.55 m → 0: free (inflation_radius)
Higher k: passes closer to tables — good in narrow rooms
Lower k: keeps away — safer, but may not fit between tables
Notes: This chart is computed from the Nav2 inflation formula with our values: robot_radius 0.22 m (inscribed radius), inflation_radius 0.55 m. Inside 0.22 m the cost is 253 — the robot would touch the obstacle, so paths never go there. Between 0.22 m and 0.55 m the cost is 252·e^(−k·(d − 0.22)), where k is cost_scaling_factor. Beyond 0.55 m the cost is 0. With k = 3 (ours) the cost stays high for a long way, so the planner keeps far from tables; with k = 10 the cost drops quickly and the robot passes closer. Exercise: change cost_scaling_factor and watch the path in RViz.

## Slide 23: Global planner: search the costmap grid for the cheapest path
Dijkstra (NavFn default, use_astar: false)
134 cells expanded · path length 21
S
G
A* (use_astar: true)
72 cells expanded · path length 21
S
G
■ expanded ■ path ■ wall Same path cost — A* uses a distance-to-goal guess to look at far fewer cells. Nav2 plans on the inflated costmap, so paths keep away from walls.
Notes: Both grids are computed with real Dijkstra and A* searches on a 16 × 10 grid with a wall (4-connected moves). Blue cells were expanded (examined) before the goal was reached; orange is the final path. Dijkstra (NavFn default, use_astar: false) spreads out evenly in all directions. A* adds a guess of the remaining distance (the heuristic), so it expands fewer cells but finds a path of the same cost. In Nav2 the cell cost comes from the costmap, so inflated cells are expensive and paths stay away from walls. Our planner settings: nav2_navfn_planner, tolerance 0.5 m, allow_unknown true. Other options students can try: Smac Planner 2D, Smac Hybrid-A*, Theta*.

## Slide 24: Controller: Regulated Pure Pursuit chases a point on the path
robot
lookahead point
arc the robot drives
L = lookahead distance
planned path
κ = 2·yL / L² ω = v · κ
y_L = sideways offset of the lookahead point
Slows down (regulates) when:
turning sharply: radius < 0.9 m
close to obstacles (cost-regulated)
near the goal: last 0.6 m, never below 0.05 m/s
Rotates in place first when the path is more than 45° away (rotate_to_heading_min_angle 0.785).
Ours: desired_linear_vel 0.18 m/s
lookahead_dist 0.4 m · 20 Hz
Notes: The controller runs 20 times per second. Pure Pursuit picks the lookahead point: the point on the path at distance L (lookahead_dist, 0.3–0.6 m, ours 0.4 m) from the robot. It then drives the circular arc that ends at that point: curvature κ = 2·y_L/L², where y_L is the sideways offset of the point in the robot frame, and ω = v·κ. “Regulated” means it slows down for sharp turns (radius below 0.9 m), near obstacles (cost-regulated) and when approaching the goal (last 0.6 m), never below 0.05 m/s. If the path points more than 45° away from the robot heading, it first rotates in place (use_rotate_to_heading). Our desired_linear_vel is 0.18 m/s. Discuss: what happens with a very short lookahead (oscillation) or a very long one (cuts corners)?

## Slide 25: A behavior tree decides what Nav2 does next — and how it recovers
NavigateRecovery
retry up to 6 times
NavigateWithReplanning
pipeline sequence
RecoveryActions
round robin
ComputePathToPose
planner · replans 1× per second
FollowPath
controller · 20 Hz
Clear costmaps
Spin
Wait
Back up
Ticked every 10 ms
bt_loop_duration: 10
Each node returns
SUCCESS · FAILURE · RUNNING
On failure
run the next recovery, then navigate again
Notes: bt_navigator runs the default tree navigate_to_pose_w_replanning_and_recovery.xml. The tree is ticked every 10 ms (bt_loop_duration) and each node answers SUCCESS, FAILURE or RUNNING. The left branch navigates: it recomputes the path once per second (so new obstacles are avoided) and runs the controller to follow it. If navigation fails, the root recovery node runs the next recovery action in round-robin order — clear the costmaps, spin, wait, back up — and then tries navigating again, up to 6 times. Behavior trees are XML files, so the behaviour can be changed without C++: for example, a tree that waits at a table for 30 s before returning home.

## Slide 26: From Nav2 to the wheels: every velocity command passes four stages
Controller
Regulated Pure Pursuit, 20 Hz
cmd_vel_nav
Velocity smoother
≤ 0.18 m/s, 0.5 rad/s, 0.4 m/s²
cmd_vel_smoothed
Collision monitor
slows / stops before a collision
/cmd_vel
esp32_driver
v, ω → v_l, v_r · 0.5 s watchdog
serial "s v_l v_r"
ESP32 + motors
PWM out, encoder ticks in
encoder ticks "e L R" → /odom
Keep the limits equal everywhere. velocity_smoother max_velocity must match esp32_driver max_linear_speed / max_angular_speed. Our driver used to clamp v and ω separately, so the robot drove a different curve than the controller planned. Now it scales both together.
Notes: Follow one velocity command. The controller (Regulated Pure Pursuit) publishes cmd_vel_nav at 20 Hz. The velocity smoother limits speed and acceleration (ours: 0.18 m/s, 0.5 rad/s, 0.4 m/s²) and publishes cmd_vel_smoothed. The collision monitor checks the LiDAR points against the robot footprint and slows down or stops before a collision; it publishes /cmd_vel. esp32_driver converts v and ω into wheel speeds, stops the motors if /cmd_vel stops for 0.5 s (watchdog), and sends "s v_l v_r" to the ESP32. The ESP32 drives the motor driver and sends encoder ticks back ("e left right"), which esp32_driver turns into /odom. Key lesson: the limits in the velocity smoother must equal the driver limits.

## Slide 27: From simulation to the real robot
04
What Gazebo did for us, what we must provide, and every change we made to the package
Notes: Module 4 is the heart of the course for this robot. Simulation hides many problems: perfect odometry, a perfect clock, the right map, and the right robot size. We go through what had to change, using the real mistakes we found in our own repository.

## Slide 28: Everything Gazebo gave for free must now come from hardware
Need | Gazebo (bcr_bot) | Real robot
Wheels follow /cmd_vel | diff_drive plugin | esp32_driver → ESP32 → MDD10A → motors
Odometry | plugin — perfect with odometry_source:=world | encoders + esp32_driver (calibrate!) or rf2o
LiDAR /scan | ray sensor plugin (16 m, 30 Hz) | sllidar_ros2 + RPLidar A1 (12 m)
base_link → laser | URDF + robot_state_publisher | static transform in robot_bringup (measure it)
Clock | Gazebo /clock (use_sim_time: true) | computer clock (use_sim_time: false)
Map | warehouse bcr_map.yaml | your room, made with slam_toolbox
Topic names | /bcr_bot/scan, /bcr_bot/cmd_vel … | /scan, /odom, /cmd_vel
Robot size | 0.9 × 0.64 m, 70 kg | ≈ 0.38 m wide — set robot_radius
Notes: Go row by row and ask students who provides each item in simulation and on the real robot. Motion: the diff_drive plugin is replaced by esp32_driver + ESP32 firmware + MDD10A motor driver. Odometry: perfect in Gazebo with odometry_source:=world; on the real robot it comes from encoders and must be calibrated. LiDAR: the ray sensor becomes the sllidar_ros2 driver. The LiDAR transform comes from a static transform publisher in robot_bringup.launch.py. Time: Gazebo publishes /clock and nodes use use_sim_time: true; on the real robot use_sim_time must be false everywhere. Map: we must build our own. Topics lose the /bcr_bot namespace. Robot size changes from 0.9 × 0.64 m to about 0.38 m wide.

## Slide 29: Real robot hardware and how the parts talk to each other
Robot computer
Raspberry Pi / laptop · Ubuntu + ROS 2
Nav2 · slam_toolbox · esp32_driver
sllidar_node · table_nav_web
Phone / laptop
web browser
RPLidar A1
360° laser scanner
Wi-Fi · HTTP :8080
USB · /scan
ESP32
counts encoder pulses, makes PWM
USB serial 115200
MDD10A
dual motor driver
PWM + DIR
2 × DC gear motors
19.2:1 · 7-pulse encoders
encoder A/B pulses
# PC → ESP32, 20 Hz
s 0.095 0.265
# ESP32 → PC, ~30 Hz
e 12345 12290
wheel speeds in m/s · encoder tick counts
Notes: Draw this on the board as you explain. The robot computer (Raspberry Pi or laptop with Ubuntu and ROS 2) runs all ROS nodes. The RPLidar connects by USB and is read by sllidar_node. The ESP32 connects by USB serial at 115200 baud: the PC sends wheel speeds in m/s 20 times per second ("s 0.095 0.265"); the ESP32 sends encoder tick counts about 30 times per second ("e 12345 12290"). The ESP32 generates PWM and direction signals for the MDD10A dual motor driver, which powers two DC gear motors (19.2:1) with 7-pulse encoders. A phone or laptop on the same Wi-Fi opens the web app on port 8080. Tip: USB ports can swap after reboot (ttyUSB0/ttyUSB1) — use /dev/serial/by-id/ names.

## Slide 30: Changes to nav2_params.yaml for the real robot
Parameter | Before | Now | Why
use_sim_time (all nodes) | True | False | No Gazebo clock on the real robot
scan topic (AMCL, costmaps) | /bcr_bot/scan | /scan | Name used by the real LiDAR driver
local_costmap robot_radius | 0.12 | 0.22 | Same as global; robot ≈ 0.38 m wide
local_costmap size | 2 × 2 m | 3 × 3 m | See obstacles before reaching them
velocity_smoother max_velocity | 0.26 m/s, 1.0 rad/s | 0.18, 0.5 | Equal to the ESP32 driver limits
velocity_smoother max_accel | 2.5 m/s² | 0.4 m/s² | Small motors slip with simulation values
AMCL laser range | −1 … 100 m | 0.2 … 12 m | RPLidar A1 range; ignore own body
progress_checker | 0.5 m in 10 s | 0.25 m in 15 s | Slow robot that also turns in place
behavior_server rotation | 1.0 rad/s | 0.5 rad/s | Spin recovery within motor limits
Notes: These are the parameter changes. The first two rows (use_sim_time and topic names) were done in an earlier commit by the team (291a5ce); the rest were added after analysing the robot (commit 809277a on branch real-robot-nav-web-app). For each row ask students what would happen without the change. For example: with use_sim_time true and no Gazebo, nodes wait forever for /clock; with max_accel 2.5 m/s² small motors slip and odometry becomes wrong; with robot_radius 0.12 the controller thinks the robot is tiny and brushes table legs.

## Slide 31: Changes to launch files and code, plus three new pieces
CHANGED
bcr_bot/launch/nav2.launch.py
map:= argument (your room), use_rviz:=; sim-only remapper removed
NEW
bcr_bot/launch/robot_bringup.launch.py
LiDAR + base_link → laser TF + ESP32 driver, exactly one odometry source
CHANGED
bcr_bot/config/nav2_params.yaml
values on the previous slide
CHANGED
my_python_pkg/…/esp32_teleop_odometry_node.py
scales v and ω together, keeping the planned curve
NEW
my_python_pkg/…/odom_check.py
prints distance and total rotation for calibration
NEW
table_nav_web/
web page + HTTP API → Nav2 NavigateToPose (“go to table1”)
NEW
ROBOT_NAV_GUIDE.md
step-by-step guide and troubleshooting
Notes: Walk through the repository on GitHub (branch real-robot-nav-web-app of github.com/febintjames/autonomousrobot). nav2.launch.py now takes a map:= argument (default ~/maps/my_map.yaml) and no longer starts remapper.py, which only renamed topics for Gazebo. robot_bringup.launch.py is the real-robot replacement for gazebo.launch.py: it starts the LiDAR driver, publishes base_link → laser and starts esp32_driver, with exactly one odometry source. The driver change keeps the turning radius when limiting speed. odom_check.py helps calibration. table_nav_web is the web app. ROBOT_NAV_GUIDE.md has the full procedure.

## Slide 32: Five mistakes that made the real robot drive badly
Mistake
What you see
Fix
1
Simulation map on a real robot
Pose jumps, paths through real walls
Map your room; nav2.launch.py map:=
2
Two odometry publishers (esp32 + rf2o)
Robot jerks, pose flickers
One source: odom_source:=wheel or laser
3
Speeds clamped separately
Robot drifts off the planned curve
Equal limits; scale v and ω together
4
Costmap robot_radius 0.12 m
Cuts corners, brushes tables
Measure the robot: robot_radius 0.22 m
5
F/B/L/R serial driver (cmd_vel_serial)
Cannot turn while driving forward
Use esp32_driver (wheel speeds)
Notes: These are real findings from our repository, which makes them great teaching material. 1) nav2.launch.py loaded the Gazebo warehouse map. 2) The rf2o launch file had been changed to publish /odom and odom → base_link, the same as esp32_driver, so two nodes fought over the robot pose. 3) Nav2 allowed 0.26 m/s and 1.0 rad/s but the driver clamped to 0.18 and 0.5 separately, changing the curve. 4) The local costmap robot_radius was 0.12 m. 5) cmd_vel_serial.py sends only F/B/L/R commands, so it cannot drive a curve — it must not be used with Nav2. Ask students to predict each symptom before revealing it.

## Slide 33: Hands-on lab
05
Six steps from an empty workspace to “go to Table 1” — each one checked before the next
Notes: Run the lab in groups of 3–4 students per robot. Each step has a clear “done when” check; do not let a group move on until it passes, because every later step depends on the earlier ones (for example, navigation cannot work with uncalibrated odometry or a wrong LiDAR transform).

## Slide 34: Lab workflow: six steps, each one checked before the next
1
Build
Done when: colcon build succeeds and the workspace is sourced
2
Bring-up
Done when: /scan and /odom publish; one odometry publisher
3
Calibrate
Done when: 1 m drive and 5 turns match odom_check
4
Map
Done when: map looks like the room; saved in ~/maps
5
Navigate
Done when: robot reaches RViz goals reliably
6
Web app
Done when: tapping “table1” drives to Table 1
Notes: Show the whole journey first. Step 1 builds the workspace. Step 2 starts the robot and checks the hardware. Step 3 calibrates odometry. Step 4 builds the map. Step 5 tests navigation from RViz. Step 6 adds the web app and saved table positions. Each “done when” line is the check the teacher signs off.

## Slide 35: Steps 1–2: build, start the robot and check the hardware
# Step 1: build (once)
cd ~/ros2_ws && colcon build --symlink-install
source install/setup.bash
# Step 2: LiDAR + TF + ESP32 driver
ros2 launch bcr_bot robot_bringup.launch.py \
lidar_port:=/dev/ttyUSB0 esp32_port:=/dev/ttyUSB1
# checks (new terminal)
ros2 topic hz /scan
ros2 topic info /odom # Publisher count: 1
ros2 run tf2_ros tf2_echo odom base_link
ros2 run teleop_twist_keyboard teleop_twist_keyboard
LiDAR
box in front shows on the red X axis in RViz — else laser_yaw:=3.14159
Odometry
exactly 1 publisher on /odom
Direction
key i → odom x increases; key j → yaw increases
Slow speed
wheels still turn at 0.05 m/s
Notes: Students type these commands themselves. Expected results: /scan at roughly 5–10 Hz; ros2 topic info /odom shows Publisher count: 1; tf2_echo prints a transform. The LiDAR direction test catches a backwards-mounted sensor: in RViz (fixed frame base_link) a box held in front of the robot must appear on the red X axis side; if it appears behind, relaunch with laser_yaw:=3.14159. The teleop test catches swapped motors or encoders. The 0.05 m/s test matters because Nav2 slows to that speed near goals; if the wheels do not turn, the firmware needs a speed PID or minimum PWM.

## Slide 36: Step 3: calibrate odometry so 1 metre in ROS is 1 metre on the floor
ros2 run my_python_pkg odom_check # → distance 0.930 m | rotation 1910.0 deg
Test 1 · drive straight 1.00 m
Mark the floor with tape and drive exactly 1.00 m.
linear_scale = 1.00 ÷ distance
Example: odom says 0.930 m → linear_scale 1.075
Test 2 · spin 5 full turns
Restart odom_check, then spin in place exactly 5 turns.
wheel_separation = 0.34 × rotation ÷ 1800
Example: odom says 1910° → wheel_separation 0.361 m
Then: write both values into bcr_bot/launch/robot_bringup.launch.py (esp32 parameters), restart, and repeat until the error is under 2 %. Do Test 1 first — linear_scale also affects rotation.
Notes: Calibration is the single biggest improvement for a real robot. odom_check prints the distance and the total rotation (not wrapped at 180°) since it started. Test 1: mark 1.00 m on the floor with tape and drive it with teleop; linear_scale = 1.00 / distance shown. Rebuild/restart with that value first, because linear_scale also affects rotation. Test 2: spin in place exactly 5 turns; wheel_separation = 0.34 × rotation / 1800. Real wheel separation usually comes out a little larger than the tape measure because the tyres scrub. Repeat until the error is below 2 %.

## Slide 37: Step 4: build a map of your room with slam_toolbox
# terminal 1: robot
ros2 launch bcr_bot robot_bringup.launch.py
# terminal 2: SLAM + RViz
ros2 launch bcr_bot mapping.launch.py
# terminal 3: drive slowly around the room
ros2 run teleop_twist_keyboard teleop_twist_keyboard
# when the map is complete
mkdir -p ~/maps
ros2 run nav2_map_server map_saver_cli -f ~/maps/my_map
Result: my_map.pgm (picture) + my_map.yaml (resolution, origin). New map → save the table places again.
Drive slowly
about 0.1–0.2 m/s and turn slowly
Close the loop
finish where you started
Visit every table
so each one is on the map
Check before saving
straight, single walls in RViz
Notes: Three terminals. Drive slowly: SLAM adds a node every 0.15 m and fast motion blurs scans. Close the loop by finishing where you started, so loop closure removes drift. Visit every table so it appears in the map. Before saving, check in RViz that walls are straight and single (a doubled wall means the robot lost track — drive back to a known area). map_saver_cli writes my_map.pgm and my_map.yaml. If the room changes a lot or you make a new map, saved table positions must be recorded again, because coordinates belong to one map.

## Slide 38: Step 5: navigate on your map
# terminal 1: robot
ros2 launch bcr_bot robot_bringup.launch.py
# terminal 2: Nav2 with YOUR map
ros2 launch bcr_bot nav2.launch.py \
map:=$HOME/maps/my_map.yaml
# headless robot: add use_rviz:=False
1
2D Pose Estimate
click where the robot is, drag the way it faces
2
Check
laser scan lines up with the map walls
3
Nav2 Goal
click a destination — the robot plans and drives
What happens after you click a goal
Goal pose
RViz or web app
BT navigator
behavior tree
Planner
path on global costmap
Controller
/cmd_vel at 20 Hz
Wheels
esp32_driver → ESP32
Notes: Start the robot and Nav2 with the map from step 4. In RViz, first use 2D Pose Estimate: click where the robot really stands and drag in the direction it faces. AMCL then publishes map → odom and the laser scan should line up with the walls; if it does not, set the pose again. Then use Nav2 Goal to send a destination. Explain the chain shown at the bottom: the goal goes to the behavior tree navigator, which calls the planner (path) and the controller (velocity), which drives the wheels. On a headless robot computer add use_rviz:=False and run RViz on a laptop on the same network (same ROS_DOMAIN_ID).

## Slide 39: Step 6: send the robot to “Table 1” from a phone
Phone browser
big buttons: table1, table2…
HTTP POST /api/goto
table_nav_web
HTTP server + ROS 2 node
action goal
Nav2
NavigateToPose action
/cmd_vel
Robot
drives to the table
feedback: distance left, ETA, arrived
Save the tables once
1 Robot is here — set the start pose on the map
2 Drive to Table 1, facing the way it should wait
3 Type table1 → Save current position
4 Tap table1 any time; STOP cancels
# start the web app
ros2 launch table_nav_web table_nav_web.launch.py
# open on a phone (same Wi-Fi)
http://<robot-ip>:8080
# from another program
curl -X POST http://<robot-ip>:8080/api/goto \
-H 'Content-Type: application/json' \
-d '{"name": "table1"}'
Notes: table_nav_web is a small ROS 2 node that is also a web server. The phone page sends JSON requests (for example POST /api/goto with {"name": "table1"}). The node looks up the saved pose in ~/.ros/table_locations.yaml and sends a NavigateToPose action goal to Nav2, then shows the feedback (distance left, ETA) on the page. STOP cancels all Nav2 goals. To save a table: set the robot pose (Robot is here), drive the robot to the table facing the way it should wait, type table1 and press Save current position. Other programs (a restaurant POS, a button box) can use the same HTTP API with curl. Security note: there is no login, so keep the robot on a private Wi-Fi.

## Slide 40: Debugging toolkit: look at the data before changing parameters
Command | What it tells you
ros2 node list | Which nodes are running
ros2 topic info -v /cmd_vel | Publishers, subscribers and message type
ros2 topic hz /scan | How often data arrives
ros2 topic echo /odom | The live values
ros2 run tf2_tools view_frames | PDF drawing of the whole TF tree
ros2 run tf2_ros tf2_echo map base_link | Where the robot is on the map
rqt_graph | Picture of nodes and topics
ros2 param get /controller_server FollowPath.desired_linear_vel | The value a parameter really has
ros2 action list | Nav2 actions such as /navigate_to_pose
Notes: Teach a habit: when something is wrong, first look at the data, then change parameters. Is the node running (ros2 node list)? Is the topic publishing, how fast, and who publishes it (ros2 topic hz, ros2 topic info -v)? Is the TF tree complete (view_frames, tf2_echo)? What value is a parameter really using (ros2 param get)? rqt_graph shows how nodes are connected. Give each group a printed copy of this slide.

## Slide 41: Troubleshooting: symptom → most likely cause → what to do
Symptom | Most likely cause | What to do
Robot snakes along the path | Odometry not calibrated, or two odometry publishers | Step 3; ros2 topic info /odom
Pose jumps in RViz | Wrong map, wrong initial pose or wrong laser yaw | Your map; 2D Pose Estimate; laser_yaw
Spins in place, never drives | Encoder or motor direction reversed | Key i / j test from Step 2
“Failed to make progress” | Motors stall at low speed | Firmware PID or raise min speeds
Stops 20–25 cm short of the table | xy_goal_tolerance: 0.25 | Lower to 0.10 after calibration
Will not pass between tables | Gap < 2 × robot_radius, or inflation too wide | Measure robot; inflation_radius 0.40
Web page: “Nav2 is not running” | Terminal not sourced or other ROS_DOMAIN_ID | source install/setup.bash
Nav2 runs, wheels never move | /cmd_vel is TwistStamped (newer Nav2) | Check type with topic info -v
Notes: Use this as a lookup table during the lab. The last row is specific to newer Nav2 releases (Kilted), where /cmd_vel can be a TwistStamped message; esp32_driver subscribes to Twist, so the message types must match. ros2 topic info -v /cmd_vel shows the type.

## Slide 42: Student exercises
BASIC
1. Map the classroom
Make and save a map, then save three tables in the web app.
BASIC
2. Measure accuracy
Send the robot to table1 ten times and measure the error with a tape. Tune xy_goal_tolerance.
INTERMEDIATE
3. Inflation experiment
Change cost_scaling_factor from 3 to 10. Does the robot pass closer to tables? Is it still safe?
INTERMEDIATE
4. Planner comparison
Set use_astar: true, then try the Smac 2D planner. Compare the paths in RViz.
INTERMEDIATE
5. Odometry comparison
Drive the same square with odom_source:=wheel and :=laser. Which drifts less?
ADVANCED
6. Sensor fusion
Fuse wheel odometry, rf2o and an IMU with robot_localization (EKF).
Notes: Exercises go from basic to advanced. 1 and 2 check that the system works and introduce measurement. 3 and 4 connect parameters to the algorithms from module 3 (inflation and planners). 5 compares odometry sources. 6 is a project for strong groups: fuse wheel odometry, rf2o and an IMU with the robot_localization EKF; then esp32_driver and rf2o publish without TF and the EKF publishes /odom and odom → base_link. Ask every group to write a one-page report with measurements, not opinions.

## Slide 43: Key takeaways and where to learn more
01
Reuse packages: the real work is configuration, calibration and glue code.
02
Simulation hides real problems: perfect odometry, a perfect clock, the wrong map.
03
One publisher per transform, equal speed limits everywhere, the real robot size.
04
Look at the data (topics, TF) before tuning parameters.
Resources
Nav2 documentation
docs.nav2.org
SLAM Toolbox
github.com/SteveMacenski/slam_toolbox
bcr_bot (original)
github.com/blackcoffeerobotics/bcr_bot
ROS 2 documentation
docs.ros.org
Our code (branch real-robot-nav-web-app)
github.com/febintjames/autonomousrobot
Notes: Close by repeating the four lessons. Point students to the resources: the Nav2 documentation explains every parameter used in nav2_params.yaml; the SLAM Toolbox README explains the mapping parameters; the original bcr_bot repository shows the simulation side; our branch real-robot-nav-web-app contains every change discussed, plus ROBOT_NAV_GUIDE.md with the full lab procedure.